TRIPLO RP wall-mounted multiple washbasin

Reference: 121750

CCTP description

Wall-mounted triple washbasin, 1,800 x 500mm.

With a splashback to protect the wall from splashing and improve hygiene.

Basin internal diameter: 310mm.

Bacteriostatic 304 stainless steel.

Polished satin finish.

Stainless steel thickness: 1.5mm.

Rounded edges prevent injury.

With central tap hole Ø 35mm.

Supplied with 1 ¼" waste.

Without overflow.

Supplied with brackets and fixing elements.

CE marked. Complies with European standard EN 14688.

Weight: 22kg.

[Formerly ref: 0211750008]