TEMPOFIX 3 with TEMPOMATIC 4 URINAL

Reference: 543006D-430016

CCTP description

Frame system W. 430mm for urinals:

Black powder- coated steel frame for wall-mounted installation.

Fixes to floor and load-bearing walls, anchoring bolts supplied.

Adjustable bracket from 100 - 280mm.

Frame height can be adjusted from 0 - 200mm.

Ø 50mm soil pipe with waterproof seal.

Delivered pre-mounted.

Complies with French standard NF D12-208.

Compatible with solid wall finishes 10 - 120mm.

Fitted with TEMPOMATIC 4 F1/2" electronic valve:

Battery-operated with 123 6V Lithium battery.

Stainless steel wall plate 145 x 145mm with integrated electronics.

Shock-resistant infrared presence detection sensor.

Waterproof recessing housing.

Detection delay is 10 seconds.

3 programmes (rinsing volume can be set according to urinal type).

High frequency mode (exclusive to DELABIE).

Hygienic duty flush every 24 hours (can be adjusted to 12 hours or Off) after last use: prevents vacuums.

Flow rate pre-set at 0.15 L/sec at 3 bar, can be adjusted.

Connection with 1/2" brass connection (for urinals supplied by flexibles).

Technical features: see TEMPOMATIC 4 urinal ref. 430PBOX-430016.

10-year warranty.