TEMPOFIX 3 wall-mounted frame system for WCs

Reference: 578300-578222

CCTP description

Wall-mounted frame system W. 350mm for wall-hung WC:

Black powder-coated steel frame.

Fixes to load-bearing floors.

Frame height can be adjusted from 0 - 200mm (with 1m mark).

Ø 32mm flush tube with Ø 55mm connection washer.

Ø 100mm soil pipe and PVC collar with waterproof seal, with 2 settings positions.

Delivered pre-mounted.

Complies with French standard NF D12-208.

For dry walls 10 - 35mm.

Fitted with TEMPOFLUX 2 time flow direct flush valve:

Ø 195mm chrome-plated wall plate with concealed fixings.

3L/6L dual flush (can be adjusted to 2L/4L).

Soft-touch operation.

Vacuum breaker.

Stopcock and flow rate/volume adjuster.

Solid brass body and shock-resistant, scale-resistant mechanism.

In-line inlet M3/4".

Acoustic level complies with European standard EN 12541 class II.

Technical features: see TEMPOFLUX 2 ref. 762902.

10-year warranty.