FACIL wall-mounted washbasin

Reference: 121800

CCTP description

Wall-mounted washbasin, 360 x 390mm.

Basin internal diameter: 320mm.

Clean and simple design.

Bacteriostatic 304 stainless steel. Polished satin finish.

Stainless steel thickness: 1.2mm.

Rounded edges prevent injury. With Ø 35mm on the right.

Supplied with 1 ¼" waste.

Without overflow.

Supplied with fixing elements.

CE marked. Complies with European standard EN 14688. Weight: 4.1kg.

[Formerly ref: 0211080006]