2506T2

Mechanical basin mixer

Reference: 2506T2

Specification Description

Mechanical basin mixer with swivelling, tubular spout H. 220mm L. 200mm Ø 22mm with smooth interior (reduced bacterial development).

High spout with BIOSAFE hygienic outlet suitable for fitting a BIOFIL terminal filter.

Ø 35mm ceramic cartridge.

Flow rate limited to 5 lpm at 3 bar.

Slimline control lever.

Without pop-up waste.

Supplied with F3/8" PEX stainless steel braided flexibles.

Chrome-plated brass body with reinforced fixing via 2 stainless steel rods and back-nuts.