2565T1

Mechanical mixer for sinks and troughs

Reference: 2565T1

Specification Description

Mechanical mixer for sinks or troughs with fixed spout H. 160mm L. 160mm.

High spout with hygienic flow straightener suitable for fitting a BIOFIL terminal filter.

Ø 40mm ceramic cartridge and pre-set maximum temperature limiter.

Body and spout with smooth interiors (reduces bacterial development).

Flow rate limited to 5 lpm at 3 bar.

Chrome-plated body, base and spout.

Hygiene control lever L. 215mm requires no manual contact.

Supplied with braided stainless steel flexibles made from PEX F3/8" 10x100.

Reinforced fixings via 2 stainless steel rods and back-nuts.