2620EP

SECURITHERM EP BIOSAFE pressure balancing basin mixer

Reference: 2620EP

Specification Description

SECURITHERM basin mixer H. 95mm L. 110mm with pressure balancing and BIOSAFE hygienic outlet integrated into the body.

Anti-scalding safety: HW flow rate is reduced if CW supply fails.

Securitouch thermal insulation prevents burns.

Ø 35mm ceramic cartridge with pressure balancing.

Pre-set maximum temperature limiter.

Thermal shocks are possible without removing the control lever or shutting off the cold water supply.

Body with smooth interior and very low water volume (reduces bacterial development).

Flow rate limited to 4 lpm at 3 bar.

Solid control lever.

Chrome-plated stainless steel body.

Ergonomic pop-up waste 1 1/4" in brass.

Reinforced fixing via two stainless steel rods.

Stainless steel braided PEX flexibles F3/8" with rotating unions and non-return valves and filters.