2871T1

Mechanical sink mixer with BIOCLIP removable spout

Reference: 2871T1

Specification Description

Mechanical sink mixer with high, swivelling, removable BIOCLIP spout H. 160mm.

Supplied with 1 disposable, recyclable Hostaform® spout L. 175mm, Ø 22mm with star-shaped flow straightener.

Ø 40mm ceramic cartridge with pre-set maximum temperature limiter.

Body and spout with smooth interiors (reduced bacterial development).

Flow rate limited to 5 lpm at 3 bar.

Chrome-plated brass body and base.

Hygiene control lever L. 215mm requires no manual contact.

Supplied with F3/8" PEX stainless steel braided flexibles, 10x100.

Reinforced fixing via 2 stainless steel rods and back nuts.