44115715

TEMPOMATIC

Electronic tap

Reference : 44115715

CCTP description

Cross wall electronic basin tap:

Independent IP65 electronic control unit.

230/12V mains supply with transformer.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 to 6 lpm.

Scale-resistant flow straightener.

Adjustable duty flush (pre-set flush ~60 sec. every 24h after last use).

Shockproof infrared presence detection sensor for wall ≤ 165mm.

Anti-blocking safety.

Solenoid valve with filter and Ø 15mm conical inlet.

Chrome-plated fixed spout L. 170mm for wall ≤ 165mm with anti-rotating pin.

Threaded rods can be cut to size.