TEMPOFIX 3 frame system for urinals

Reference: 543006-430016

CCTP description

Frame system W. 430mm for urinals:

Black powder-coated steel frame for wall-mounted installation.

Fixes to floor and load-bearing walls with anchoring bolts supplied.

Adjustable bracket 100 - 280mm.

Frame height can be adjusted from 0 - 200mm.

Ø 50mm soil pipe with waterproof seal.

Delivered pre-mounted.

Complies with French standard NF D12-208.

Compatible with wall finishes 13 - 120mm.

Fitted with TEMPOMATIC 4 F1/2" direct flush electronic valve:

Operated by 123 6V Lithium batteries.

Bright stainless steel plate 145 x 145mm with integrated electronics.

Shock-resistant infrared presence detection sensor.

Waterproof recessing housing.

Detection delay is 10 seconds.

3 programmes (rinsing volume can be adjusted according to urinal type).

High frequency mode (exclusive to DELABIE).

Flow rate pre-set at 0.15 L/sec at 3 bar, can be adjusted.

Hygienic duty flush every 24 hours (can be adjusted to 12 hours or OFF) after last use: prevents vacuums.

Connection with Ø 35mm connection washer (for standard urinal valves).

Technical features: see TEMPOMATIC 4 urinal ref. 430PBOX-430016.

10-year warranty.