578305DE-578222

TEMPOFIX 3 self-supporting frame system for WCs

Reference: 578305DE-578222

CCTP description

Self-supporting frame system W. 350mm for wall-hung WCs:

- Black powder-coated steel frame.

- Fixes to load-bearing floors.

- Frame height can be adjusted from 0 to 200mm (with 1m mark).

- Ø 32mm flush tube with Ø 55mm connection washer.

- Ø 110mm HDPE soil pipe with waterproof seal, with 2 settings positions.

- Delivered pre-mounted.

- Complies with French standard NF D12-208.

- For dry walls 10 - 35mm.

Fitted with TEMPOFLUX 2 time flow direct flush valve:

- Ø 195mm chrome-plated wall plate with concealed fixings.

- 3L/6L dual flush (can be adjusted to 2L/4L).

- Soft-touch operation.

- Vacuum breaker.

- Stopcock and flow rate/volume adjuster.

- Solid brass body and shock-resistant, scale-resistant mechanism.

- In-line inlet M3/4".

- Acoustic level complies with European standard EN class II.

Technical characteristics: see TEMPOFLUX 2 ref. 762902.

10-year warranty.