74250015

TEMPOSOFT MIX 2

Reference : 74250015

CCTP description

Deck-mounted time flow basin mixer:

Soft-touch operation.

Time flow ~7 sec.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 to 6 lpm.

Tamperproof scale-resistant flow straightener.

Chrome-plated solid brass body.

PEX flexibles with stopcocks, filters, non-return valves and Ø 15mm conical inlets.

Fixing reinforced by 2 stainless steel rods.

Side temperature control with standard lever and maximum temperature limiter.