TEMPOSTOP

Reference: 746001

CCTP description

TEMPOSTOP wall-mounted time flow basin tap:

Time flow ~7 seconds.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 - 6 lpm.

Tamperproof, scale-resistant flow straightener.

Solid chrome-plated brass body M1/2" .

AB anti-blocking system: water will flow only when the push-button is released.

10-year warranty.