TEMPOSTOP shower valve

Reference: 747000

CCTP description

Time flow shower valve for exposed installation:

TEMPOSTOP M1/2" time flow valve for mixed water supply.

For wall-mounted installation.

Straight for in-line inlet.

Time flow ~15 seconds.

Flow rate pre-set at 9 lpm at 3 bar, can be adjusted.

Chrome-plated solid brass body and push-button.

10-year warranty.