TEMPOFLUX 2

Reference: 762150

CCTP description

Cross wall time flow valve for direct flush:

For walls ≤ 140mm.

3L/6L dual flush can be adjusted to 2L/4L.

Soft-touch operation.

Vacuum breaker.

Integrated stopcock and flow rate / flush volume adjuster.

Solid brass body.

Chrome-plated metal push-button.

In-line inlet M3/4".

Outlet connection for PVC tube Ø 26/32mm.

Threaded rod can be cut to size.

Acoustic level complies with European standard EN 12541 class II.

Base flow rate: 1 L/sec.

Suitable for Rimless WC pans.

10-year warranty.