TEMPOFLUX 2 WC flush valve 6L

Reference: 762901

CCTP description

Recessed time flow valve for direct flush:

Multipurpose recessing housing.

Chrome-plated metal wall plate Ø 195mm.

Recessing depth can be adjusted from 0 - 20mm.

6L single flush.

Soft-touch operation.

Vacuum breaker.

Integrated stopcock and flow rate / flush volume adjuster.

Solid brass body.

Chrome-plated metal push-button.

In-line inlet M3/4".

Outlet connection for PVC tube Ø 26/32mm.

Acoustic level complies with European standard EN 12541 class II.

Base flow rate: 1 L/sec.

Suitable for rimless WC pans.

10-year warranty.

This model does not have a waterproof recessing housing. The installer must ensure that the recessing area is waterproof and any leaks or condensation can drain away (see installation guide).