TEMPOFLUX recessed urinal 1/2"

Reference: 778BOX-778700

CCTP description

Waterproof recessed time flow valve for individual urinals:

Satin finish stainless steel wall plate 145 x 145mm.

Chrome-plated metal push-button.

Waterproof recessing housing:

- Collar with waterproof seal.

- Hydraulic connection to the outside and maintenance from the front.

- Adjusts to all types of installation (rails, solid walls, panels).

- Compatible with wall finishes from 10 - 120mm (while maintaining the minimum recessing depth of 83mm).

- Suitable for standard or "pipe-in-pipe" supply.

- Stopcock and flow rate adjustment, filter and cartridge all integrated and accessible from the front.

- TEMPOFLUX F1/2" flush valve is compatible with sea water and grey water.

- Supplied in 2 kits: secure system flush without sensitive elements.

Soft-touch operation.

Time flow pre-set at ~3 seconds, can be adjusted from 3 - 7 seconds (patented).

Flow rate pre-set at 0.15 l/sec at 3 bar, can be adjusted up to 0.3 L/sec.

Complies with European standard EN 12541 (class II acoustic level).

Connection with Ø 35mm connection washer (for standard urinals) or 1/2" brass connection (for urinals supplied by flexible).

For use with neck tube ref. 752430 or 757430.

10-year warranty.