TEMPOMIX

Reference: 790BOX-790218

CCTP description

Recessed time flow shower mixer:

Tamperproof bright polished stainless steel wall plate 160 x 220mm.

Waterproof recessing housing.

10-30mm allowance for different wall finishes.

TEMPOMIX 3/4" single control mixer.

Ligature-resistant collar.

Temperature control and operation via the push-button.

Maximum temperature limiter (can be adjusted by the installer).

Time flow ~30 seconds, soft-touch operation.

Flow rate 12 lpm at 3 bar, can be adjusted.

Concealed fixings, stopcocks M1/2".

Integrated non-return valves and filters.

Chrome-plated metal push-button.

10-year warranty.