TEMPOMIX 3 shower kit

Reference: 794BOX1-794219

CCTP description

Recessed time flow shower mixer with soft-touch operation:

Tamperproof chrome-plated metal wall plate 160 x 160mm.

Waterproof recessing housing:

- Collar with waterproof seal.

- Hydraulic connection from the exterior and maintenance from the front.

- Top inlet.

- Adjusts to all types of installation (rails, solid walls, panels).

- Compatible with wall finishes 10 - 120mm (while maintaining the minimum recessing depth of 93mm).

- Suitable for standard pipe supply or "pipe in pipe".

- Stopcocks and flow rate adjustment, filters, non-return valves and cartridge are integrated and can be accessed from the front.

- TEMPOMIX 3 single control mixer F½".

-Supplied in 2 kits: secure system flush without sensitive elements.

Temperature control and operation via the push-button.

Maximum temperature limiter (can be adjusted by installer).

Time flow ~30 seconds, can be adjusted.

Soft-touch operation.

Flow rate 6 lpm at 3 bar.

Chrome-plated, tamperproof, scale-resistant ROUND shower head with automatic flow rate regulation.

10-year warranty.