TEMPOMIX 3 time flow mixer

Reference: 794BOX3-794200

CCTP description

TEMPOMIX 3 recessed time flow basin mixer:

Tamperproof chrome-plated metal plate 160 x 160mm.

Waterproof recessing housing:

- Collar with waterproof seal.

- Hydraulic connection from the outside and maintenance from the front.

- Adjusts to all types of installations (rails, solid walls, panels).

- Compatible with wall finishes 10 - 120mm (while maintaining the minimum recessing depth of 93mm).

- Suitable for standard or "pipe in pipe" supply.

- Stopcocks and flow rate adjustment, filters, non-return valves and cartridge are all integrated and accessible from the front.

- TEMPOMIX 3 single control mixer F½".

- Supplied in 2 kits: secure system flush without sensitive elements.

Temperature control and operation via the push-button.

Maximum temperature limiter (can be adjusted by installer).

Time flow ~7 seconds, can be adjusted.

Soft-touch operation.

Flow rate pre-set at 3 lpm at 3 bar pressure, can be adjusted 1.5 - 6 lpm.

Scale-resistant flow straightener.

Spout L. 110mm with smooth interior and low water volume (reduces niches where bacteria can develop).

10-year warranty.

Provisional availability 1st half 2019, please contact the sales office to check availability.