TEMPOMIX

Reference: 79500015

CCTP description

Deck-mounted single control time flow basin mixer.

Soft-touch operation.

Temperature control and operation via the push-button.

Time flow ~7 seconds.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 - 6 lpm.

Scale-resistant flow straightener.

Chrome-plated solid brass body.

Ergonomic chrome-plated metal push-button.

PEX flexibles Ø 15mm for compression fittings with stopcocks, filters and non-return valves.

Fixing reinforced by 2 stainless steel rods.

Adjustable maximum temperature limiter.

10-year warranty.