H963015

SECURITHERM Sequential thermostatic shower mixer

Reference: H963015

Specification Description

SECURITHERM thermostatic sequential individual shower mixer.

Opens and closes with cold water.

No risk of cross flow between hot and cold water.

Mixer with no non-return valves on the inlets (reduces bacterial proliferation).

Anti-scalding failsafe: shuts off immediately if cold water supply fails (and vice versa).

Securitouch thermal insulation prevents burns.

Scale-resistant thermostatic sequential cartridge adjusts the flow rate and the temperature. <br/>Temperature can be adjusted from cold water to 39°C with maximum temperature limiter set at 39°C.

Thermal shocks are possible.

Body with smooth interior and low water volume (reduces niches where bacteria can develop).

Flow rate regulated at 9 lpm.

Chrome-plated brass body and Hygiene control lever L. 100mm.

M1/2" bottom outlet.

Supplied with M1/2" M3/4" inline STOP/CHECK, ideal for hospitals.

10-year warranty.