SECURITHERM basin mixer H. 210mm L. 150mm

Reference: H9726

CCTP description

SECURITHERM thermostatic dual control basin mixer, with swivelling spout L. 150mm H. 210mm, with ergonomic pop-up waste 1 1/4" in brass.

Anti-scalding failsafe: hot water shuts off immediately if cold water supply fails.

Spout with smooth interior and with BIOSAFE hygienic outlet, suitable for fitting a BIOFIL filter (reduces bacterial development).

Scale-resistant thermostatic cartridge for temperature control.

¼-turn ceramic head for adjusting the flow rate.

Temperature can be adjusted, with two temperature limiters: first temperature limiter set at to 38°C (can be overidden), and second temperature limiter set at 41°C.

Thermal shocks are possible without removing the control knob or shutting off the cold water supply.

Flow rate limited to 5 lpm at 3 bar.

ERGO controls.

Reinforced fixing via 2 stainless steel rods.

Supplied with braided stainless steel flexibles made from PEX F3/8" with filters and non-return valves.

10-year warranty.