SECURITHERM dual control thermostatic shower mixer

Reference: H9739

CCTP description

SECURITHERM individual dual control thermostatic shower mixer with:

- Anti-scalding safety: hot water shuts off immediately if cold water supply fails (and vice versa).

- Scale-resistant thermostatic cartridge for temperature adjustment.

- 1/4-turn ceramic head for flow rate adjustment.

- Temperature control from 25 - 40°C with maximum temperature limiter set at 38°C.

- Thermal shocks are possible without removing the control knob or shutting off the cold water.

- Flow rate regulated at 9 lpm.

- Chrome-plated brass body and CLASSIC controls.

- M1/2" shower outlet.

- M3/4" inlets with integrated filters and non-return valves.

- Mixer with offset STOP/PURGE wall connectors, M1/2" M3/4", ideal for hospitals.

10-year warranty.